## Slide 1
MODERN ADVANCES IN COMPUTATIONAL IMAGING AT MICROWAVE AND MILLIMETRE-WAVE FREQUENCIES
Okan Yurduseven#1, Thomas Fromentèze#2
#1Queen’s University Belfast, UK
#2Xlim Research Institute, University of Limoges, France
1okan.yurduseven@qub.ac.uk, 2thomas.fromenteze@unilim.fr
STh-01

## Slide 2
New advances in computational imaging:
Polarimetric imaging, phaseless imaging, and recent advances in antenna systems and k-space reconstruction techniques
Okan Yurduseven#1, Thomas Fromenteze#2
#1Queen’s University Belfast, UK
#2Xlim Research Institute, University of Limoges, France
1okan.yurduseven@qub.ac.uk, 2thomas.fromenteze@unilim.fr
STh-01

## Slide 3
STh-01
Outlines of the second part
Acceleration of image reconstruction: k-space and Fourier processing
Computational polarimetric imaging
Computational phaseless imaging

## Slide 4
STh-01
Accelerating computational imaging with Fourier processing
Some problems require the estimation of millions of voxels
Fromenteze, T., Yurduseven, O., Berland, F., Decroze, C., Smith, D. R., & Yarovoy, A. G. (2019). A Transverse Spectrum Deconvolution Technique for MIMO Short-Range Fourier Imaging.
IEEE Transactions on Geoscience and Remote Sensing.
Using MIMO apertures, the number of measured samples can also reach very large numbers
M
Transmitters × Receivers × Frequency samples
nbx × nby × nbz
Sensing matrix
Example
Transmitters : 40 × 40
Receivers : 40 × 40
Frequency points : 20
nbx : 300
nby : 200
nbz : 300
size(H) = 51.10⁶× 18.10⁶
Raw memory consumption ~2200 Tb (single precision)

## Slide 5
STh-01
What makes Fourier processing so efficient?
Note: Explanations are given for a set of 2D examples. For the sake of simplicity, we use an asymptotic form of Hankel's functions:
Propagation is modelled within a scalar model: waves progress from source points in a spherical manner.
© Walt Disney pictures
Notes: H_0^{(2)}(k r) \approx \frac{e^{-jkr}}{\sqrt{r}}
G(r,r_a) = \frac{e^{-jk\lvert r - r_a \lvert }}{\lvert r- r_a \lvert}

## Slide 6
STh-01
Weyl's expansion:
with:
Following an angular spectrum decomposition, a spherical wave is analogous to a sum of plane waves
What makes Fourier processing so efficient?
Notes: \frac{e^{-jkr}}{r} = \frac{j}{2\pi} \iint e^{-j(k_x x + k_z z + \lvert k_y \lvert y)}\, dk_x dk_z
k_y = \sqrt{k^2 - k_x^2 - k_z^2}

## Slide 7
STh-01
Impact of a spatial Fourier transform on measurements:
The transformation helps to identify a set of angles of arrival
What makes Fourier processing so efficient?
Notes: Left right

## Slide 8
STh-01
Impact of a spatial Fourier transform on measurements:
The transformation helps to identify a set of angles of arrival
What makes Fourier processing so efficient?
Notes: Up down

## Slide 9
STh-01
What makes Fourier processing so efficient?
A fundamental concept for short-range Fourier imaging: the definition of a dispersion relation
An association of transmitted and received plane waves are considered:
Product of Tx and Rx Green's functions: sum of the arguments of their exponential functions
(the rigorous demonstration is not that straightforward)
In the SIMO case:
A single Tx plane wave interacts with a set of Rx plane waves
We choose an area to image whose center is called the stationary phase point.
Notes: k_y = k \sin(\theta_t) + \sqrt{k^2 - k_x^2}

## Slide 10
STh-01
What makes Fourier processing so efficient?
Full process for image computation:
1. Fourier transform and variable change
2. Back-propagation
3. Inverse Fourier transform
Note: 1. The back-propagation step can be greatly accelerated using Stolt interpolation instead of a summation.
2. In this example, we add an additional phase shift to compensate for the offset of the transmit antenna.
This approach is often referred as the Range Migration Algorithm (RMA) or k-ω algorithm
Lopez-Sanchez, J. M., & Fortuny-Guasch, J. (2000). 3-D radar imaging using range migration techniques. IEEE Transactions on antennas and propagation, 48(5), 728-737.
Zhuge, X., & Yarovoy, A. G. (2012). Three-dimensional near-field MIMO array imaging using range migration techniques. IEEE Transactions on Image Processing, 21(6), 3026-3033.
Code available here https://bit.ly/2XGCVbH
Notes: S(k_x,y) = \int S(k_x,k) e^{j ( k(y+\Delta_y) + \sqrt{k^2-k_x^2}\, y)}dk
S(k_x,y) = \int S(k_x,k)\, e^{j \overbrace{(k + \sqrt{k^2-k_x^2})}^{k_y} y}dk
I(x,y) = \mathfrak{F}^{-1}(S(k_x,y))

## Slide 11
STh-01
Making Fourier techniques compatible with computational imaging
Problem: the use of frequency-diverse antenna does not grant us direct access to the spatial dimension
Measurement of a "compressed" signal:
Identification of signals in the radiating aperture
How to efficiently retrieve the signals in the aperture?
Notes: g = \int_{r_r} {\color{red} \int_{r} G(r_t,r) f(r) G(r,r_r)\ d^3 r }\ C(r_r)\, d^2 r_r
{\color{red} s_\omega(r_r) = \int_{r} G_\omega(r_t,r)\ f(r) G_\omega(r,r_r)\ d^3 r }

## Slide 12
STh-01
Making Fourier techniques compatible with computational imaging
Problem: the use of frequency-diverse antenna does not grant us direct access to the spatial dimension
Measurement of a "compressed" signal
Identification of signals in the radiating aperture
The signals undergo a known distortion
In matrix form
with
Problem: a simple matrix inversion reconstruction requires the sacrifice of a dimension
with
Pros: we just retrieved our lost spatial dimension
Cons: our frequency dimension is now missing
Notes: \rho = \sum_{r_r} H \odot {\color{red} s}
{\color{red} \hat{s}_{eq}} = H^+ \odot (\rho,...,\rho)

## Slide 13
STh-01
Making Fourier techniques compatible with computational imaging
Problem: the use of frequency-diverse antenna does not grant us direct access to the spatial dimension
An estimation is carried out using an equalization
The measurement can also be written as a Hadamard product (element-wise multiplication)
with
The measured "compressed" signal is multiplied by each line of the pseudo-inverse matrix
The signals reconstructed in the radiating aperture can finally be used to reconstruct images using Fourier techniques.
Notes: \rho_\omega = \int_{r_r} {\color{red} \int_{r} G_\omega(r_t,r) f(r) G_\omega(r,r_r)\ d^3 r } \ H_\omega(r_r) d^2 r_r
{\color{red} s_\omega(r_r) = \int_{r} G_\omega(r_t,r)\ f(r) G_\omega(r,r_r)\ d^3 r }
\rho_\ = \int_{r_r} {s_\omega(r_r)} \ H_\omega(r_r) d^2 r_r
\rho_\omega = H_\omega \color{red} s_\omega^T
\rho \in \mathbb{C}^{n_f \times 1}
{\color{red} s_\omega} \in \mathbb{C}^{1 \times n_{r_r}}
{\color{red}\hat{s}_\circ} = H^+\rho

## Slide 14
STh-01
Performance comparison : Equalization+RMA VS full-matrix approach
Fromenteze, T., Kpré, E. L., Decroze, C., Carsenat, D., Yurduseven, O., Imani, M., ... & Smith, D. R. (2015, September). Unification of compressed imaging techniques in the microwave range and deconvolution strategy. In 2015 European Radar Conference (EuRAD) (pp. 161-164). IEEE.
Equalization+RMA
Full-matrix approach
 | Pre-computation time | Computation time
Eq+RMA | 4.8 s | 2.4 s
Full-matrix | 38 min | 66 s
Data presented in 2015, significant progress has been made on both methods since

## Slide 15
STh-01
Examples of implementations
Fromenteze, T., Decroze, C., & Carsenat, D. (2014). Waveform coding for passive multiplexing: Application to microwave imaging. IEEE Transactions on Antennas and Propagation, 63(2), 593-600.
Frequency range: 2-4 GHz
7 fps (limited by communication times between equipment)
From 4 antennas to 1 receiver

## Slide 16
STh-01
Fromenteze, T., Kpré, E. L., Decroze, C., & Carsenat, D. (2015, September). Passive UWB beamforming: AN to M compression study. In 2015 European Radar Conference (EuRAD) (pp. 169-172). IEEE.
Frequency range: 2-4 GHz​
From 16 antennas to 4 receivers
Examples of implementations
Fromenteze, T., Decroze, C., Abid, S., & Yurduseven, O. (2018). Sparsity-Driven Reconstruction Technique for Microwave/Millimeter-Wave Computational Imaging. Sensors, 18(5), 1536.
Improvement of the equalization technique by a sparsity-driven technique based on Toeplitz matrices

## Slide 17
STh-01
Fromenteze, T., Kpré, E. L., Carsenat, D., Decroze, C., & Sakamoto, T. (2016). Single-shot compressive multiple-inputs multiple-outputs radar imaging using a two-port passive device. IEEE Access, 4, 1050-1060.
Frequency range: 2-10 GHz​
Going MIMO: From 24x24 antennas to 1 transceiver
Examples of implementations
Image computation: 1.5 s with MIMO RMA

## Slide 18
STh-01
Fromenteze, T., Yurduseven, O., Berland, F., Decroze, C., Smith, D. R., & Yarovoy, A. G. (2019). A Transverse Spectrum Deconvolution Technique for MIMO Short-Range Fourier Imaging. IEEE Transactions on Geoscience and Remote Sensing.
Improving the MIMO RMA
Bottleneck of the RMA: interpolating the Tx and Rx plane waves
Plane wave fusion can be computationally intensive
Everything else can be done from Fast-Fourier transforms
Notes: \hat{\sigma}(x,y,z) = k_{y_T} k_{y_R} \int_{k_x} \int_{k_y} \int_{k_z} S(k_{x_T},k_{z_T},k_{x_R},k_{z_R},k) e^{j k_y y} e^{j k_x x} e^{j k_z z} dk_x dk_y dk_z

## Slide 19
STh-01
Fromenteze, T., Yurduseven, O., Berland, F., Decroze, C., Smith, D. R., & Yarovoy, A. G. (2019). A Transverse Spectrum Deconvolution Technique for MIMO Short-Range Fourier Imaging. IEEE Transactions on Geoscience and Remote Sensing.
Improving the MIMO RMA
The initial approach is quite abstract and based on asymptotic developments of radiation integrals

## Slide 20
STh-01
Fromenteze, T., Yurduseven, O., Berland, F., Decroze, C., Smith, D. R., & Yarovoy, A. G. (2019). A Transverse Spectrum Deconvolution Technique for MIMO Short-Range Fourier Imaging. IEEE Transactions on Geoscience and Remote Sensing.
Improving the MIMO RMA
Introducing the transverse spectrum deconvolution (TSD RMA)
Core idea: it's all about radiation patterns
Main advantages:
- more intuitive and visual approach
- k-space patterns depend only on the spatial sampling not on the frequency

## Slide 21
STh-01
Fromenteze, T., Yurduseven, O., Berland, F., Decroze, C., Smith, D. R., & Yarovoy, A. G. (2019). A Transverse Spectrum Deconvolution Technique for MIMO Short-Range Fourier Imaging. IEEE Transactions on Geoscience and Remote Sensing.
Improving the MIMO RMA
Core idea: it's all about radiation patterns
Main advantages:
- more intuitive and visual approach
- k-space patterns depend only on the spatial sampling not on the frequency
Interrogation of a spectrum through known radiation patterns
Tx radiation patterns
Rx radiation patterns
Target spectrum
Expression in matrix form and separation of spatial variables
Reconstruction of transverse spectral data by pseudo-inversion
1. Interpolation calculations are replaced by matrix multiplication
2. These calculations are made without any frequency dependence
3. RAM consumption is greatly reduced
4. Reconstructions are more accurate
Notes: S = \int_{k_x} \int_{k_z} {\color{red} P_t(k_x-k_{x_t},k_z-k_{z_t})}\, {\color{DarkGreen} S_c(k_x,k_z,k)} {\color{blue} P_r(k_x-k_{x_r},k_z-k_{z_r})}\ dk_x\ dk_z
S(k) = {\color{Magenta} P_x}\ {\color{DarkGreen} S_c(k)} \ {\color{Magenta} P_z}
{\color{DarkGreen} \hat{S}_c(k)} = {\color{Magenta} P_x^+}\ S(k) \ {\color{Magenta} P_z^+}

## Slide 22
STh-01
Fromenteze, T., Yurduseven, O., Berland, F., Decroze, C., Smith, D. R., & Yarovoy, A. G. (2019). A Transverse Spectrum Deconvolution Technique for MIMO Short-Range Fourier Imaging. IEEE Transactions on Geoscience and Remote Sensing.
Improving the MIMO RMA
Definition of a new state of the art of range-migration algorithms
Application to large and densely populated MIMO arrays
Validation with a MIMO array of 71⁴ radiating elements
more than 25 million interactions at each frequency
Notes: S = \int_{k_x} \int_{k_z} {\color{red} P_t(k_x-k_{x_t},k_z-k_{z_t})}\, {\color{DarkGreen} S_c(k_x,k_z,k)} {\color{blue} P_r(k_x-k_{x_r},k_z-k_{z_r})}\ dk_x\ dk_z
S(k) = {\color{Magenta} P_x}\ {\color{DarkGreen} S_c(k)} \ {\color{Magenta} P_z}
{\color{DarkGreen} \hat{S}_c(k)} = {\color{Magenta} P_x^+}\ S(k) \ {\color{Magenta} P_z^+}

## Slide 23
STh-01
Polarimetric computational imaging
Motivation: Study of anisotropic/multiple-bounce scattering
Far-field: Estimation of soil parameters
Short-range: Threat detection
Unsupervised Terrain Classification Preserving Polarimetric Scattering Characteristics"
J-S Lee, M.R. Grunes, E. Pottier, L. Ferro-Famil - IEEE TGRS, 2004
Holographic arrays for multi-path imaging artifact reduction"
D.L. McMakin, D.M. Sheen, T.E. Hall - US Patent, 2005

## Slide 24
STh-01
Polarimetric computational localization
Conventional approach
Computational approach
Doubles the hardware constraints compared to scalar systems
Fromenteze, T., Boyarsky, M., Yurduseven, O., Gollub, J., Marks, D. L., & Smith, D. R. (2017, July). Computational polarimetric localization with a radiating metasurface. In 2017 IEEE International Symposium on Antennas and Propagation & USNC/URSI National Radio Science Meeting (pp. 407-408). IEEE.

## Slide 25
STh-01
Polarimetric computational localization
Measured signal
Fromenteze, T., Boyarsky, M., Yurduseven, O., Gollub, J., Marks, D. L., & Smith, D. R. (2017, July). Computational polarimetric localization with a radiating metasurface. In 2017 IEEE International Symposium on Antennas and Propagation & USNC/URSI National Radio Science Meeting (pp. 407-408). IEEE.
Polarized sources
Dyadic Green's function
Transfer function of the cavity
(3 polarizations on its surface)
We now get out of the scalar approximation
To lighten the notation, frequencies are implicit
=
in the polarization space:
Notes: g = \int_{r_a} \int_r \overline{C}(r_a) \overline{\overline{G}}(r,r_a) \overline {s}(r) dr_a dr
g = \overline{C}\, \overline{\overline{G}} \overline{s}
\overline{\overline{G}}(r,r_a) = (1 + \frac{1}{k^2} \Delta \Delta\, \cdot ) \frac{\exp(-j k \lvert r - r_a \lvert )}{\lvert r - r_a \lvert }\ \overline{\overline{I\, }}

## Slide 26
STh-01
Polarimetric computational localization
Measured signal
Fromenteze, T., Boyarsky, M., Yurduseven, O., Gollub, J., Marks, D. L., & Smith, D. R. (2017, July). Computational polarimetric localization with a radiating metasurface. In 2017 IEEE International Symposium on Antennas and Propagation & USNC/URSI National Radio Science Meeting (pp. 407-408). IEEE.
We now get out of the scalar approximation
To lighten the notation, frequencies are implicit
Discrete model
Reconstruction
Notes: g = \int_{r_a} \int_r \overline{C}(r_a) \overline{\overline{G}}(r,r_a) \overline {s}(r) dr_a dr
g = \overline{C}\, \overline{\overline{G}} \overline{s}
\overline{\overline{G}}(r,r_a) = (1 + \frac{1}{k^2} \Delta \Delta\, \cdot ) \frac{\exp(-j k \lvert r - r_a \lvert )}{\lvert r - r_a \lvert }\ \overline{\overline{I\, }}
\hat{\overline{s}} = \left( \overline{\overline{G}}\, \overline{C} \right)^+ g

## Slide 27
STh-01
Polarimetric computational localization
Fromenteze, T., Boyarsky, M., Yurduseven, O., Gollub, J., Marks, D. L., & Smith, D. R. (2017, July). Computational polarimetric localization with a radiating metasurface. In 2017 IEEE International Symposium on Antennas and Propagation & USNC/URSI National Radio Science Meeting (pp. 407-408). IEEE.
Near field scans
Cavity quality factor Q~12 000
Notes: g = \int_{r_a} \int_r \overline{C}(r_a) \overline{\overline{G}}(r,r_a) \overline {s}(r) dr_a dr
g = \overline{C}\, \overline{\overline{G}} \overline{s}
\overline{\overline{G}}(r,r_a) = (1 + \frac{1}{k^2} \Delta \Delta\, \cdot ) \frac{\exp(-j k \lvert r - r_a \lvert )}{\lvert r - r_a \lvert }\ \overline{\overline{I\, }}

## Slide 28
STh-01
Polarimetric computational imaging
Fromenteze, T., Boyarsky, M., Yurduseven, O., Gollub, J., Marks, D. L., & Smith, D. R. (2017, July). Computational polarimetric localization with a radiating metasurface. In 2017 IEEE International Symposium on Antennas and Propagation & USNC/URSI National Radio Science Meeting (pp. 407-408). IEEE.
Near field scans
Spatial correlations:
Notes: g = \int_{r_a} \int_r \overline{C}(r_a) \overline{\overline{G}}(r,r_a) \overline {s}(r) dr_a dr
g = \overline{C}\, \overline{\overline{G}} \overline{s}
\overline{\overline{G}}(r,r_a) = (1 + \frac{1}{k^2} \Delta \Delta\, \cdot ) \frac{\exp(-j k \lvert r - r_a \lvert )}{\lvert r - r_a \lvert }\ \overline{\overline{I\, }}

## Slide 29
STh-01
Polarimetric computational localization
Fromenteze, T., Boyarsky, M., Yurduseven, O., Gollub, J., Marks, D. L., & Smith, D. R. (2017, July). Computational polarimetric localization with a radiating metasurface. In 2017 IEEE International Symposium on Antennas and Propagation & USNC/URSI National Radio Science Meeting (pp. 407-408). IEEE.
-5dB isosurfaces
- Frequency range : 18.5-26 GHz
- 801 Frequency samples
- 134 × 36 × 134 ~ 650 000 voxels
- Volume of 0.8 × 0.75 × 0.8 m³
- Computed in less than a second using Fourier processing
Reconstruction
Notes: g = \int_{r_a} \int_r \overline{C}(r_a) \overline{\overline{G}}(r,r_a) \overline {s}(r) dr_a dr
g = \overline{C}\, \overline{\overline{G}} \overline{s}
\overline{\overline{G}}(r,r_a) = (1 + \frac{1}{k^2} \Delta \Delta\, \cdot ) \frac{\exp(-j k \lvert r - r_a \lvert )}{\lvert r - r_a \lvert }\ \overline{\overline{I\, }}

## Slide 30
STh-01
Polarimetric computational imaging
Scalar imaging forward model
measured frequency-domain signal
scalar Tx electric field
scalar Rx electric field
scalar reflectivity function (Δε(r))
If our target exhibits anisotropic/depolarizing behavior:
polarization conversion
Each point in space must be defined as a susceptibility tensor
The scattered field then interacts with the Rx aperture
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.
Notes: \overline{E_i}^{sca}(r) = {\color{blue} \overline{E_i}(r)} {\color{DarkGreen} \overline{\overline{\chi}}(r)}
g_{i,j}(\omega) = \int_r {\color{blue} \overline{E_i} (r)} {\color{DarkGreen} \overline{\overline{\chi}}(r)}\, {\color{red} \overline{E_j} (r)^T}\, dr

## Slide 31
STh-01
Polarimetric computational imaging
Forward model of the polarimetric imaging problem
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.
Operating with two panels
Operating with a single two-ports panel
Tx E-field
Rx E-field
Notes: \overline{E_i}^{sca}(r) = {\color{DarkGreen} \overline{\overline{\chi(r)}}}\, {\color{blue} \overline{E_i}(r)}
g_{i,j}(\omega) = \int_r {\color{red} \overline{E_j} (r)}\, {\color{DarkGreen} \overline{\overline{\chi(r)}}}\, {\color{blue} \overline{E_i} (r)}\, dr

## Slide 32
STh-01
Polarimetric computational imaging
Forward model of the polarimetric imaging problem
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.
Understanding the physics behind the susceptibility tensors:
The electrons within the target medium are represented by a simple mechanical model
Rotation matrix
Diagonalized tensor
Notes: \overline{E_i}^{sca}(r) = {\color{DarkGreen} \overline{\overline{\chi(r)}}}\, {\color{blue} \overline{E_i}(r)}
g_{i,j}(\omega) = \int_r {\color{red} \overline{E_j} (r)}\, {\color{DarkGreen} \overline{\overline{\chi(r)}}}\, {\color{blue} \overline{E_i} (r)}\, dr
{\color{DarkGreen} \overline{\overline{\chi}}(r) = \overline{\overline{R}}(r) \text{diag}(\bar \xi(r))\overline{\overline{R}}(r)^T}

## Slide 33
STh-01
Polarimetric computational imaging
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.
Eigendecompositions helps to identify the directions of the main axis of the tensors (eigenvectors) and the associated eigenvalues define the anisotropic behavior of each voxel
Isotropic scattering
Anisotropic scattering
Understanding the physics behind the susceptibility tensors:
The electrons within the target medium are represented by a simple mechanical model
Rotation matrix
Diagonalized tensor
Notes: \overline{E_i}^{sca}(r) = {\color{DarkGreen} \overline{\overline{\chi(r)}}}\, {\color{blue} \overline{E_i}(r)}
g_{i,j}(\omega) = \int_r {\color{red} \overline{E_j} (r)}\, {\color{DarkGreen} \overline{\overline{\chi(r)}}}\, {\color{blue} \overline{E_i} (r)}\, dr
{\color{DarkGreen} \overline{\overline{\chi}}(r) = \overline{\overline{R}}(r) \text{diag}(\bar \xi(r))\overline{\overline{R}}(r)^T}

## Slide 34
STh-01
Polarimetric computational imaging
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.
Analogy with diffusion tensor imaging Magnetic Resonance Imaging
https://en.wikipedia.org/wiki/File:DiffusionMRI_glyphs.png
https://www.siemens-healthineers.com/magnetic-resonance-imaging/options-and-upgrades/clinical-applications/syngo-dti-tractography
The main axis analysis of the tensors reconstructed in each voxel makes it possible to reconstruct the path of the fibers in the brain
Understanding the physics behind the susceptibility tensors:
The electrons within the target medium are represented by a simple mechanical model
Rotation matrix
Diagonalized tensor
Notes: \overline{E_i}^{sca}(r) = {\color{DarkGreen} \overline{\overline{\chi(r)}}}\, {\color{blue} \overline{E_i}(r)}
g_{i,j}(\omega) = \int_r {\color{red} \overline{E_j} (r)}\, {\color{DarkGreen} \overline{\overline{\chi(r)}}}\, {\color{blue} \overline{E_i} (r)}\, dr
{\color{DarkGreen} \overline{\overline{\chi}}(r) = \overline{\overline{R}}(r) \text{diag}(\bar \xi(r))\overline{\overline{R}}(r)^T}

## Slide 35
STh-01
Polarimetric computational imaging
Forward model of the polarimetric imaging problem
Solving the inverse problem
The Tx and Rx vector fields are inversed to reveal the interaction between each couple of polarization states
Criteria to be met to ensure successful reconstruction
The radiated fields in transmission and reception must be simultaneously orthogonal in three domains:
- in frequency
- in polarization
- spatially
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.
Notes: {\color{DarkGreen} \hat{\overline{\overline{\chi}}}(r)} = {\color{blue} \overline{E_i}(r)^+} g_{i,j}\, {\color{red} \overline{E_j}(r)^+}

## Slide 36
STh-01
Polarimetric computational imaging
Computing the spatial correlation for each pair of ports and polarizations
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.
Notes: {\color{DarkGreen} \hat{\overline{\overline{\chi}}}(r)} = {\color{blue} \overline{E_i}(r)^+} g_{i,j}\, {\color{red} \overline{E_j}(r)^+}

## Slide 37
STh-01
Polarimetric computational imaging
Experimental validation
Imaging targets made with thin copper wires
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.
Number of frequency samples: 3601
Frequency range: 17.5-26.5 GHz

## Slide 38
STh-01
Polarimetric computational imaging
Results with the letter D
Reconstructed from the measurement of a single frequency-domain signal
For each voxel
9 tensor elements (only 6 are independent)
each tensor element is a complex value
The diversity of representations of such tensors remains unexplored for these applications
x and z are the transverse axis, y is the longitudinal (propagation) axis
Special feature of the short-range polarimetric imaging
We obtain projections on the propagation axis
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.

## Slide 39
STh-01
Polarimetric computational imaging
Results with the letter D
Reconstructed from the measurement of a single frequency-domain signal
x and z are the transverse axis, y is the longitudinal (propagation) axis
Extraction of a cross-section plan
The phase is included in the reconstructions and can be color-coded to reveal more information
The results are still based Born first approximation
we must keep a critical eye on the analysis of the results
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.

## Slide 40
STh-01
Polarimetric computational imaging
Improvements with basic processing
Correlation of transverse components
Optimized SNR noise reduced by the coherent sum of the useful parts of the tensor
Anisotropic behavior orientation of copper wires revealed by the phase information
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.
Notes: \hat{\chi}_{corr}(r) = \hat{\chi}_{x,x}(r) \cdot \hat{\chi}_{z,z}(r)^*

## Slide 41
STh-01
Polarimetric computational imaging
Going further with eigendecompositions
The diagonalization of the tensors is computed for each voxel on the real and imaginary parts separately
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.
Notes: \hat{\chi}_{corr}(r) = \hat{\chi}_{x,x}(r) \cdot \hat{\chi}_{z,z}(r)^*

## Slide 42
STh-01
Polarimetric computational imaging
Going further with eigendecompositions
RGB color-coding according to the orientation of the main axis of each ellipsoid
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.
Notes: \hat{\chi}_{corr}(r) = \hat{\chi}_{x,x}(r) \cdot \hat{\chi}_{z,z}(r)^*

## Slide 43
STh-01
Polarimetric phaseless imaging
In conclusion of this work
Conventional MIMO polarimetric system
Computational MIMO polarimetric system
Double the hardware constraints compared to systems based on the scalar approximation
Very few applications in short range imaging due to these limitations
Requires a single measurement chain provided that a full scan of the near fields is carried out
Paves the way for volumetric reconstruction of susceptibility tensors
Fromenteze, T., Yurduseven, O., Boyarsky, M., Gollub, J., Marks, D. L., & Smith, D. R. (2017). Computational polarimetric microwave imaging. Optics express, 25(22), 27488-27505.

## Slide 44
STh-01
Phaseless computational imaging
Conventional MIMO system
Phase measurement also creates heavy hardware constraints on each measurement chain
Motivation for this work
is it possible to reconstruct images from the intensity measurement of signals that interacted with a target?
In other words, can we replace our VNAs with spectrum analyzers and a little mathematics?
Are computational systems compatible with/supportive of these objectives?

## Slide 45
STh-01
Phaseless computational imaging
First concern: phase information is crucial
Phase swap
2D Fourier
transform

## Slide 46
STh-01
Phaseless computational imaging
First concern: phase information is crucial
After the phase swap and an inverse 2D Fourier transform

## Slide 47
STh-01
Phaseless computational imaging
Key element: phase information can however be encoded in the intensity information
Signals received in an aperture in the presence of two isotropic point sources
Interferences of complex contributions:
Transformation of phase information into intensity fluctuation
Inverse problem solving: Phase retrieval algorithms

## Slide 48
STh-01
Phaseless computational imaging
Objective: Application to microwave imaging
Expression of the measured signals
Matrix formalism
Reconstruction by pseudo-inversion
Intensity measurement: Reflectivity reconstruction?
Notes: s(r_t,r_r) = \int_r G(r_t,r_r) \sigma(r) G(r,r_r) d^3r
s_I = \lvert s \lvert ^2 = \lvert H \sigma \lvert ^2

## Slide 49
STh-01
Phaseless computational imaging
Intensity measurement: Reflectivity reconstruction?
Solving an optimization problem
Convex programming
Example: CVX and Matlab
Iterative algorithm
Example: Truncated Wirtinger Flow
Candes, E. J., Li, X., & Soltanolkotabi, M. (2015). Phase retrieval via Wirtinger flow: Theory and algorithms. IEEE Transactions on Information Theory, 61(4), 1985-2007.
Notes: s(r_t,r_r) = \int_r G(r_t,r_r) \sigma(r) G(r,r_r) d^3r
s_I = \lvert s \lvert ^2 = \lvert H \sigma \lvert ^2

## Slide 50
STh-01
Phaseless computational imaging
Experimental validation: SAR PhaseLess imaging
Complex measurements
Intensity measurements
Aperture size: 60 × 60 cm²
Number of samples: 61 × 61 = 3721
Background measurement (without marbles)
The results converge towards those obtained with phase measurement
Once again, the hardware constraint is transferred to the software layer
Notes: s(r_t,r_r) = \int_r G(r_t,r_r) \sigma(r) G(r,r_r) d^3r
s_I = \lvert s \lvert ^2 = \lvert H \sigma \lvert ^2

## Slide 51
STh-01
Phaseless computational imaging
Fromenteze, T., Liu, X., Boyarsky, M., Gollub, J., & Smith, D. R. (2016). Phaseless computational imaging with a radiating metasurface. Optics express, 24(15), 16760-16776.
Cavity-based phaseless localization
First step: localizing a source from an intensity measurement
ν1 = 23 GHz - ν2 = 23.002 GHz
The diversity of the magnitudes of near-field scans is the basis for encoding information
Notes: s(r_t,r_r) = \int_r G(r_t,r_r) \sigma(r) G(r,r_r) d^3r
s_I = \lvert s \lvert ^2 = \lvert H \sigma \lvert ^2

## Slide 52
STh-01
Phaseless computational imaging
Fromenteze, T., Liu, X., Boyarsky, M., Gollub, J., & Smith, D. R. (2016). Phaseless computational imaging with a radiating metasurface. Optics express, 24(15), 16760-16776.
Cavity-based phaseless localization
First step: localizing a source from an intensity measurement
The diversity of the magnitudes of near-field scans is the basis for encoding information
Reconstruction from the measurement of two signals on the output ports of the cavity
Algorithm: Truncated Wirtinger Flow
Number of spatial samples: 20 × 20 × 10
Number of frequency samples: 3601
Frequency range: 17.5-26.5 GHz
Notes: s(r_t,r_r) = \int_r G(r_t,r_r) \sigma(r) G(r,r_r) d^3r
s_I = \lvert s \lvert ^2 = \lvert H \sigma \lvert ^2

## Slide 53
STh-01
Phaseless computational imaging
Cavity-based phaseless imaging
Switching to the interrogation of a reflectivity function
Yurduseven, O., Fromenteze, T., Marks, D. L., Gollub, J. N., & Smith, D. R. (2017). Frequency-diverse computational microwave phaseless imaging. IEEE Antennas and Wireless Propagation Letters, 16, 2808-2811.
Small object for the determination of the point spread function
Use of a more advanced technique based on the sparsity of the scene to be imaged
Yuan, Z., Wang, H., & Wang, Q. (2019). Phase retrieval via sparse wirtinger flow. Journal of Computational and Applied Mathematics, 355, 162-173.
Notes: s(r_t,r_r) = \int_r G(r_t,r_r) \sigma(r) G(r,r_r) d^3r
s_I = \lvert s \lvert ^2 = \lvert H \sigma \lvert ^2

## Slide 54
STh-01
Phaseless computational imaging
Cavity-based phaseless imaging
Switching to the interrogation of a reflectivity function
Yurduseven, O., Fromenteze, T., Marks, D. L., Gollub, J. N., & Smith, D. R. (2017). Frequency-diverse computational microwave phaseless imaging. IEEE Antennas and Wireless Propagation Letters, 16, 2808-2811.
Key parameter: ratio M/N
M number of measurements
N number of voxels
M/N = 0.3
M/N = 0.8
Complex measurement
Sparse
WF
Regular
WF
M/N = 0.6
Comparison of the performances achieved by the different approaches
Notes: s(r_t,r_r) = \int_r G(r_t,r_r) \sigma(r) G(r,r_r) d^3r
s_I = \lvert s \lvert ^2 = \lvert H \sigma \lvert ^2

## Slide 55
STh-01
Phaseless computational imaging
Complex-based reconstruction
Phaseless reconstruction
Yurduseven, O., Fromenteze, T., Marks, D. L., Gollub, J. N., & Smith, D. R. (2017). Frequency-diverse computational microwave phaseless imaging. IEEE Antennas and Wireless Propagation Letters, 16, 2808-2811.

## Slide 56
Interesting feature of phaseless imaging: relaxes the phase coherency requirements for applications where large apertures are needed
STh-01
Phaseless computational imaging
Complex-Based
Phaseless
Yurduseven, O., Fromenteze, T., & Smith, D. R. (2018). Relaxation of alignment errors and phase calibration in computational frequency-diverse imaging using phase retrieval. IEEE Access, 6, 14884-14894.
Without phase error
With phase error
Without phase error
With phase error
Without phase error
With phase error

## Slide 57
MODERN ADVANCES IN COMPUTATIONAL IMAGING AT MICROWAVE AND MILLIMETRE-WAVE FREQUENCIES
Okan Yurduseven#1, Thomas Fromentèze#2
#1Queen’s University Belfast, UK
#2Xlim Research Institute, University of Limoges, France
1okan.yurduseven@qub.ac.uk, 2thomas.fromenteze@unilim.fr
STh-01